## Slide 1: Arithmetic Circuits
Igor Smirnov

## Slide 2: Topics of The Lecture
Register-Transfer Level (RTL)
Gates
Devices (Transistors)
Circuits
Physics
Fig.: Position in the layers of abstraction

## Slide 3: Refresher: Adder
s0
c0
x0
y0
x0
y0
s0
c0
HA
xi
yi
ci
si
HA
HA
ci-1
xi
yi
si
ci
FA
ci-1
xi | yi | ci-1 | si | ci
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
x0 | y0 | s0 | c0
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Half Adder (HA)
Full Adder (FA)
Fig.: truth table of HA
Fig.: truth table of FA
Fig.: HA schematic
Fig.: FA schematic
Fig.: HA symbol
Fig.: FA symbol
take into account the carry from the previous digit

## Slide 4: Ripple-Carry Adder
What about subtraction and negative numbers?
x0
y0
s0
HA
c0
x1
y1
s1
FA
c1
x2
y2
s2
FA
ci-1
xn-1
yn-1
sn-1
FA
cn-1
Fig.: schematic of N-digit Ripple-Carry Adder
…
Overflow detection
If cn-1 = 1, then result cannot fit into n digits

## Slide 5: Negative Numbers
How to do subtraction?
Sign-magnitude: MSB ≡ bit[n-1] is 0 for positive and 1 for negative
  Range for n-bit digit: to
  Problem 1: two representation for zero: 0000… and 1000…
  Problem 2 (more important): need a subtractor scheme different from adder
Twos complement representation allows using the adder logic for both addition and subtraction
  Negative of A is (!A + 1)
  Let’s elaborate
→ How to represent negative numbers?
Notes: Twos complement representation - Дополнительный код

## Slide 6: Twos Compliment Representation
Asymmetric range: to
One representation for zero
Representation on n-digit number:
  A =
  Example: 101 = 1 = -3
How to convert to negative?
How to do subtraction via addition?
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
addition
subtraction
overflow

## Slide 7: Example of subtraction (1)
Example: 2 – 3 = ?
  2 – 3 = 2 + (-3)
  2 + (-3) = 010 + 101 = 111
  111 = -1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1

## Slide 8: Example of subtraction (2)
Example: -1 – 3 = ?
  -1 – 3 = -1 + (-3)
  -1 + (-3) = 111 + 101 = 1100
  100 = -4
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1

## Slide 9: Overflow
Example: -2 – 3 = ?
  -2 – 3 = -2 + (-3)
  -2 + (-3) = 110 + 101 = 1011
  011 = 3 → Overflow 
Overflow conditions
  negative + negative = positive
  positive + positive = negative
How to check in HW?
  If Cn-1 != Cn-2 then overflow
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1

## Slide 10: Convert to Negative
How to convert to negative?
  School math: – B = (-1 – B) + 1
  What is (-1 – B)?
  Thus, – B = !B + 1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
1 | … | 1 | 1 | 1
Bn-1 |  | B2 | B1 | B0
-1
B
–
!B
1 | … | 1 | 1 | 1
Bn-1 |  | B2 | B1 | B0
!Bn-1 |  | !B2 | !B1 | !B0
→ Inversion

## Slide 11: Example of Converting to Negative (1)
Example: -3 = ?
  -3 = !3 + 1
  -3 = !(011) + 001 = 100 + 001 = 101
  -3 = 101
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1

## Slide 12: Example of Converting to Negative (2)
Example: -B = 110, B = ?
  B = - (-B)
  B = (!(-B)+ 1)
  B = !(110) + 001 = 001 + 001 = 010 = 2
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1

## Slide 13: Adder/Subtractor Schematic
x0
s0
FA
c0
x1
s1
FA
c1
x2
s2
FA
ci-1
xn-1
sn-1
FA
cn-1
Fig.: schematic of N-digit Ripple-Carry Adder/Subtractor
…
0
1
0
1
0
1
0
1
yn-1
!yn-1
y2
!y2
y1
!y1
y0
!y0
…
subtract?
cn-2
overflow
Calculation time is O(n)
  Carry of each digit depends on the carry of the previous digit
Can we do faster?

## Slide 14: Carry Delay
Carry calculation requires switching 2 gates in worst case
Delay of n-digit ripple adder:
  T ≈ n*2t, where t is gate delay
xi
yi
si
ci-1
ci

## Slide 15: Carry Lookahead Adder
Can we calculate carry faster?
Propagate/generate functions
Is it faster?
xi | yi | ci-1 | ci | Carry status
0 | 0 | 0 | 0 | kill
0 | 1 | 0 | 0 | propagate
1 | 0 | 0 | 0 | propagate
1 | 1 | 0 | 1 | generate
0 | 0 | 1 | 0 | kill
0 | 1 | 1 | 1 | propagate
1 | 0 | 1 | 1 | propagate
1 | 1 | 1 | 1 | generate

## Slide 16: 4-digit Carry Lookahead Adder
Fig.: Carry Lookahead Adder schematic
Fig.: Carry-lookahead circuit
T = t + log2(n + 1)*t + log2(n + 1)*t ≈ 2log2(N)*t
Compare to ripple adder: T ≈ 2N*t

## Slide 17: Carry-select Adder
Consists of two ripple carry adders and a multiplexer
  Speculatively calculate sum twice (in case carry is 0 & 1)
  Correct sum carry-out selected with the mux once the correct carry-in is known
Optimal delay occurs for a block size of
  16-bit adder’s delay: 4xFA delays + 3xMUX delays.
Fig.: Basic block of a carry select adder
Fig.: 16-bit carry select adder where each chunk is 4 bits

## Slide 18: Multiplication
The simplest way to multiply numbers is to do multiple addition
1 | 0 | 1 | 1
1 | 1 | 1 | 0
0 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 0 | 1 | 1
1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
+
+
+
+
a
b
p0
p1
p2
p3
P
+
+
+
+

## Slide 19: p-generation
a[3]
a[1]
p0[1]
p1[2]
p2[3]
p3[4]
a[3]
a[3]
p0[3]
p1[4]
p2[5]
p3[6]
p3[2]
p3[1]
p3[0]
p2[1]
p2[0]
p1[0]
0
a[0]
a[3]
b[0]
b[1]
b[2]
b[3]
p0[0]
p1[1]
p2[2]
p3[3]
a[3]
b[0]
b[1]
b[2]
b[3]
p0[0]
p1[1]
p2[2]
p3[3]
a[0]
a[3]
a[2]
p0[2]
p1[3]
p2[4]
p3[5]
a[3]
a[2]

## Slide 20: Multiplier
+
+
+
P
p-generator
p0
p1
p2
p3
b[3]
a[3]
b[2]
a[2]
b[1]
a[1]
b[0]
a[0]

## Slide 21: Questions?