## Slide 1: Finite State Machines Part 1
Igor Smirnov

## Slide 2: Recap: Sequential Logic
Combinational Logic
Memory Device
Store the current state of the circuit
Next state
Current state
Input
Output
Synchronization
allows to update the state

## Slide 3: Today’s topic
Finite State Machines
  Abstract away combinational and sequential logic into functions
  These functions take in a stream of bits, do something with them, and output something deterministic
A convenient way to conceptualize computation over time
Function can be represented with a state transition diagram
With combinational logic and registers, any FSM can be implemented in hardware!
Credits: CS61C – Sequential Logic, FSMs by Nick Riasanovsky

## Slide 4: Design of Simple Counter
5-state counter repeats 5 numbers in a sequence
  The numbers are 000, 010, 011, 101, 110
How to implement it? From what to start?
  Step 1: State transition diagram
  Step 2: State transition table
000
C | B | A
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
C+ | B+ | A+
0 | 1 | 0
x | x | x
0 | 1 | 1
1 | 0 | 1
x | x | x
1 | 1 | 0
0 | 0 | 0
x | x | x
Present state
Next state
Fig.: State Diagram
Fig.: State Transition Table
110
101
011
010

## Slide 5: Design of Simple Counter (cont.)
Counter design procedure
  Step 1: State transition diagram
  Step 2: State transition table
  Step 3: Next-state functions
C | B | A
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
C+ | B+ | A+
0 | 1 | 0
x | x | x
0 | 1 | 1
1 | 0 | 1
x | x | x
1 | 1 | 0
0 | 0 | 0
x | x | x
Present state
Next state
Fig.: State Transition Table
 | 00 | 10 | 11 | 01
0 | 0 | 0 | 0 | x
1 | x | 1 | x | 1
BC
A
 | 00 | 10 | 11 | 01
0 | 1 | 1 | 0 | x
1 | x | 0 | x | 1
BC
A
C+
B+
 | 00 | 10 | 11 | 01
0 | 0 | 1 | 0 | x
1 | x | 1 | x | 0
BC
A
A+
→ C+ = A
→ B+ = !A!C +!B
→ A+ = B!C

## Slide 6: Design of Simple Counter (cont.)
Counter design procedure
  Step 1: State transition diagram
  Step 2: State transition table
  Step 3: Next-state functions
  Step 4: Schematic
A
D
Q
C
D
Q
B
D
Q
A
!C
B
!B
!C
!A
C+ = A
B+ = !A!C +!B
A+ = B!C
Fig.: Next-state functions
Fig.: 5-state counter schematic

## Slide 7: Self-starting counters
Is our design robust?
  What if the counter jumps to 111 state (e.g., due to noise disturbance)?
Invalid states should transition to valid ones
  Assures startup
  Assures bit-error tolerance
Design your counters to be self-starting
  Draw all states in the state diagram
  Fill in the entire state-transition table
  May limit your ability to exploit don't cares
    Choose startup transitions that minimize the logic
001
100
111
Is such loop possible?
000
110
101
011
010
If yes → stuck in invalid states

## Slide 8: Make 5-state Counter Self-Starting
 | 00 | 10 | 11 | 01
0 | 0 | 0 | 0 | x
1 | x | 1 | x | 1
BC
A
 | 00 | 10 | 11 | 01
0 | 1 | 1 | 0 | x
1 | x | 0 | x | 1
BC
A
C+
B+
 | 00 | 10 | 11 | 01
0 | 0 | 1 | 0 | x
1 | x | 1 | x | 0
BC
A
A+
→ C+ = A
→ B+ = !A!C +!B
→ A+ = B!C
0
1
1
1
1
0
0
0
0
→ OK
→ OK
→ OK
C | B | A
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
C+ | B+ | A+
0 | 1 | 0
1 | 1 | 0
0 | 1 | 1
1 | 0 | 1
0 | 1 | 0
1 | 1 | 0
0 | 0 | 0
1 | 0 | 0
Present state
Next state
Fig.: State Transition Table
000
110
101
011
010
001
100
111
Fig.: State Diagram

## Slide 9: FSM is more than counters
FSM: A system that visits a finite number of logically distinct states
Counters are simple FSMs
  Outputs and states are identical
  Visit states in a fixed sequence independent on inputs
FSMs are typically more complex than counters
  Outputs can depend on current state and on inputs
  State sequencing depends on current state and on inputs

## Slide 10: FSM Design
Counter design procedure
  Step 1: State transition diagram
  Step 2: State transition table
  Step 3: Next-state functions
  Step 4: Schematic
FSM design procedure
  Step 1: State transition diagram
  Step 2: State transition table
  Step 3: State minimization
  Step 4: State encoding
  Step 5: Next-state functions
  Step 6: Schematic

## Slide 11: Two Methods for FSM Minimization
Row matching
  Easier to do by hand
  Misses minimization opportunities
Implication table
  Guaranteed to find the most reduced FSM
  More complicated algorithm
← next lecture

## Slide 12: Example: sequence analyzer
Conditions:
  Scheme has one input and one output
  Output 1 if the previous three inputs are 011 or 110
Intput/output trace example:
Let’s create the state diagram
in | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | …
out | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | …
Sequence Analyzer FSM
Sequence
1
Match
1

## Slide 13: Sequence Analyzer: straightforward diagram
X
[0]
1
[0]
10
[0]
100
[0]
101
[0]
11
[0]
110
[1]
111
[0]
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
[0]
01
[0]
011
[1]
010
[0]
00
[0]
001
[0]
000
[0]
0
1
0
1
0
1
0
0
1
0
1
0
1
0
1

## Slide 14: Transition Table Minimization: step 1
Input Sequence | Present State | Next State |  | Output
 |  | In=0 | In=1 | 
Reset | Sx | S0 | S1 | 0
0 | S0 | S00 | S01 | 0
1 | S1 | S10 | S11 | 0
00 | S00 | S000 | S001 | 0
01 | S01 | S010 | S011 | 0
10 | S10 | S100 | S101 | 0
11 | S11 | S110 | S111 | 0
000 | S000 | S0 | S1 | 0
001 | S001 | S0 | S1 | 0
010 | S010 | S0 | S1 | 0
011 | S011 | S0 | S1 | 1
100 | S100 | S0 | S1 | 0
101 | S101 | S0 | S1 | 0
110 | S110 | S0 | S1 | 1
111 | S111 | S0 | S1 | 0
Notes: Equivalent States: for all input combinations, states transition to the same or equivalent states
Algorithmic Approach • Start with state transition table • Identify states with same output behavior • If such states transition to the same next state, they are equivalent • Combine into a single new renamed state • Repeat until no new states are combined

## Slide 15: Transition Table Minimization: step 2
Input Sequence | Present State | Next State |  | Output
 |  | In=0 | In=1 | 
Reset | Sx | S0 | S1 | 0
0 | S0 | S00 | S01 | 0
1 | S1 | S10 | S11 | 0
00 | S00 | S000 | S001 | 0
01 | S01 | S010 | S011 | 0
10 | S10 | S100 | S101 | 0
11 | S11 | S110 | S111 | 0
000 | S000 | S0 | S1 | 0
001 | S001 | S0 | S1 | 0
010 | S010 | S0 | S1 | 0
011 | S011 | S0 | S1 | 1
100 | S100 | S0 | S1 | 0
101 | S101 | S0 | S1 | 0
110 | S110 | S0 | S1 | 1
111 | S111 | S0 | S1 | 0
Sno
new state
Syes
new state
Notes: Equivalent States: for all input combinations, states transition to the same or equivalent states

## Slide 16: Transition Table Minimization: step 2
Input Sequence | Present State | Next State |  | Output
 |  | In=0 | In=1 | 
0 | S0 | S00 | S01 | 0
1 | S1 | S10 | S11 | 0
00 | S00 | Sno | Sno | 0
01 | S01 | Sno | Syes | 0
10 | S10 | Sno | Sno | 0
11 | S11 | Syes | Sno | 0
Not 011/110 or Reset | Sno | S0 | S1 | 0
011/110 | Syes | S0 | S1 | 1
Sno2
new state

## Slide 17: Minimized FSM
Input Sequence | Present State | Next State |  | Output
 |  | In=0 | In=1 | 
0 | S0 | Sno2 | S01 | 0
1 | S1 | Sno2 | S11 | 0
00/10 | Sno2 | Sno | Sno | 0
01 | S01 | Sno | Syes | 0
11 | S11 | Syes | Sno | 0
Not 011/110 or Reset | Sno | S0 | S1 | 0
011/110 | Syes | S0 | S1 | 1
no
[0]
1
[0]
no2
[0]
11
[0]
1
0
1
0
1
0
1
0
[0]
01
[0]
0
1
1
0
yes
[1]
0
1
0
Fig.: State Transition Table
Fig.: State Diagram
No more rows to match

## Slide 18: Minimized vs. Initial FSM
Minimization allows using less elements (gates, latches)
  Faster FSM has a shorter critical path
  Smaller power/area
Fig.: Initial State Diagram
Fig.: Minimized State Diagram

## Slide 19: Real-life Example: Vending Coffee Machine
Conditions:
  15₵ for a cup of coffee
  Take only 5₵ and 10₵ coins
  Do no provide any change
Vending Machine FSM
Make a coffee
Coin Sensor
Start
F
T
Reset
Clock
Receive 5₵
Receive 10₵

## Slide 20: FSM design procedure
Step 1: State transition diagram
Step 2: State transition table
Step 3: State minimization
Step 4: State encoding
Step 5: Next-state functions
Step 6: Schematic

## Slide 21: Vending Machine FSM: step 1 and 2
S0
From S4, S5, S6, S7, S8
S2
T
S6
[start]
T
S4
[start]
T
S1
F
S3
F
S5
[start]
F
S8
[start]
T
S7
[start]
F
Current state | F | T | Nest state | Start
S0 | 0 | 0 | S0 | 0
 | 0 | 1 | S2 | 0
 | 1 | 0 | S1 | 0
 | 1 | 1 | x | x
S1 | 0 | 0 | S1 | 0
 | 0 | 1 | S4 | 0
 | 1 | 0 | S3 | 0
 | 1 | 1 | x | x
S2 | 0 | 0 | S2 | 0
 | 0 | 1 | S6 | 0
 | 1 | 0 | S5 | 0
 | 1 | 1 | x | x
S3 | 0 | 0 | S3 | 0
 | 0 | 1 | S8 | 0
 | 1 | 0 | S7 | 0
 | 1 | 1 | x | x
S4/S5/S6/S7/S8 | x | x | S0 | 1
!F and !T
!F and !T
!F and !T
!F and !T
S0
S0
S0
S0
S0

## Slide 22: Vending Machine FSM: step 3
Current state | F | T | Nest state | Start
S0 | 0 | 0 | S0 | 0
 | 0 | 1 | S2 | 0
 | 1 | 0 | S1 | 0
 | 1 | 1 | x | x
S1 | 0 | 0 | S1 | 0
 | 0 | 1 | S4 | 0
 | 1 | 0 | S3 | 0
 | 1 | 1 | x | x
S2 | 0 | 0 | S2 | 0
 | 0 | 1 | S6 | 0
 | 1 | 0 | S5 | 0
 | 1 | 1 | x | x
S3 | 0 | 0 | S3 | 0
 | 0 | 1 | S8 | 0
 | 1 | 0 | S7 | 0
 | 1 | 1 | x | x
S4/S5/S6/S7/S8 | x | x | S0 | 1
Current state | F | T | Nest state | Start
S0 | 0 | 0 | S0 | 0
 | 0 | 1 | S2 | 0
 | 1 | 0 | S1 | 0
 | 1 | 1 | x | x
S1 | 0 | 0 | S1 | 0
 | 0 | 1 | S4’ | 0
 | 1 | 0 | S3 | 0
 | 1 | 1 | x | x
S2 | 0 | 0 | S2 | 0
 | 0 | 1 | S4’ | 0
 | 1 | 0 | S4’ | 0
 | 1 | 1 | x | x
S3 | 0 | 0 | S3 | 0
 | 0 | 1 | S4’ | 0
 | 1 | 0 | S4’ | 0
 | 1 | 1 | x | x
S4’ | x | x | S0 | 1
Current state | F | T | Nest state | Start
S0 | 0 | 0 | S0 | 0
 | 0 | 1 | S2’ | 0
 | 1 | 0 | S1 | 0
 | 1 | 1 | x | x
S1 | 0 | 0 | S1 | 0
 | 0 | 1 | S4’ | 0
 | 1 | 0 | S2’ | 0
 | 1 | 1 | x | x
S2’ | 0 | 0 | S2’ | 0
 | 0 | 1 | S4’ | 0
 | 1 | 0 | S4’ | 0
 | 1 | 1 | x | x
S4’ | x | x | S0 | 1

## Slide 23: Minimized FSM
S1
[0]
S0
[0]
F
S2’
[1]
S4’
[1]
!F and !T
!F and !T
F
F or T
!F and !T
T
X
T
Current state | F | T | Nest state | Start
S0 | 0 | 0 | S0 | 0
 | 0 | 1 | S2’ | 0
 | 1 | 0 | S1 | 0
 | 1 | 1 | x | x
S1 | 0 | 0 | S1 | 0
 | 0 | 1 | S4’ | 0
 | 1 | 0 | S2’ | 0
 | 1 | 1 | x | x
S2’ | 0 | 0 | S2’ | 0
 | 0 | 1 | S4’ | 0
 | 1 | 0 | S4’ | 0
 | 1 | 1 | x | x
S4’ | x | x | S0 | 1

## Slide 24: Minimized FSM
Current state | 5₵ | 10₵ | Nest state | Start
0₵ | 0 | 0 | 0₵ | 0
 | 0 | 1 | 10₵ | 0
 | 1 | 0 | 5₵ | 0
 | 1 | 1 | x | x
5₵ | 0 | 0 | 5₵ | 0
 | 0 | 1 | 10₵ | 0
 | 1 | 0 | ≥15₵ | 0
 | 1 | 1 | x | x
10₵ | 0 | 0 | 10₵ | 0
 | 0 | 1 | ≥15₵ | 0
 | 1 | 0 | ≥15₵ | 0
 | 1 | 1 | x | x
≥15₵ | x | x | 0₵ | 1
5₵
0₵
10₵
≥15₵
Nothing paid
Nothing paid
5₵ or 10₵
Nothing paid
10₵
always
5₵
5₵
Make coffee
10₵

## Slide 25: Step 4, 5 and 6
Do the rest steps on your own!

## Slide 26: Backup