## Slide 1: Boolean Algebra and Combinational Circuits
Igor Smirnov

## Slide 2: Topics of The Lecture
Boolean Algebra
  math apparatus for Digital Circuits
Combinational Circuits
  Circuits without memory: their output is defined by the given input only
  Examples: all arithmetic (adder, multiplier, etc.), decoder, multiplexer and much more
Register-Transfer Level (RTL)
Gates
Devices (Transistors)
Circuits
Physics
Fig.: Position in the layers of abstraction

## Slide 3: Digital Abstraction
Logic 1
Logic 0
To design an electrical circuit we need to deal with real physical properties
In the abstraction of Digital circuits we reduce all physical properties to 0 and 1 states
It cannot be a stable state: should not occur in the circuit except during transitions from one state to the other
Logic 1
Weak 1
Weak 0
1.2
1.0
0.2
voltage
Logic 0
0.0
undefined
Supply voltage
Ground
Fig.: Maxwell’s equations
→ complicated for large systems
X

## Slide 4: Boolean Algebra
Boolean Algebra works with objects that can have only two states (true and false, or 1 and 0)
  Such object is called a Boolean object (term bit of information is used in CS)
  Boolean Algebra defines operations on Boolean objects → Boolean operations and functions
  It is convenient to represent these operations and functions via truth tables:
George Boole
(1815 – 1864)
English mathematician, philosopher and logician
c = F(a,b)
b
a
c
Fig.: Boolean function
Fig.: Truth table
a | b
0 | 0
0 | 1
1 | 0
1 | 1
c
c

## Slide 5: Main Operations
x * y
The simplest Boolean operation is …
x
!x
x
0
1
AND (or Boolean multiplication)
inversion (NOT)
x * y
x
y
x | y
0 | 0
0 | 1
1 | 0
1 | 1
0
0
0
1
! x
1
0

## Slide 6: Main Operations (2)
x | y
0 | 0
0 | 1
1 | 0
1 | 1
x  y
x + y
OR (Boolean addition)
XOR (exclusive OR, addition by module 1)
x + y
x
y
x | y
0 | 0
0 | 1
1 | 0
1 | 1
0
1
1
1
x + y = !x*y + x*!y
x
y
0
1
1
0

## Slide 7: Boolean Functions
F
Boolean operation can be combined into functions
F(x, y, z) = x + !y*z
x
y
z
x + !y*z
x | y | z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
… | … | …
0
1
0
0
1
…

## Slide 8: Main axioms/laws
De Morgan's laws | !(xy) = !x + !y | !(x + y) = !x * !y
Distributive law | x*y + z = (x + z)(y + z) | (x + y)*z = x*z + y*z
Associative law | (x*y)*z = x*(y*z) | (x + y) + z = x + (y + z)
Commutative law | x*y = y*x | x + y = y + x
Inverse law | !x*x = 0 | !x + x = 1
Idempotent law | x*x = x | x + x = x
Identity law | 1*x = x | 0 + x = x
Axiom | AND form | OR form
Null law | 0*x = 0 | 1 + x = 1

## Slide 9: Main axioms/laws
Identity law | 1*x = x | 0 + x = x
Axiom | AND form | OR form
Null law | 0*x = 0 | 1 + x = 1
x | y
0 | y
1 | y
AND and OR can be used as a logical key
Useful to reconstruct a function from the given truth table
x * y
0 (closed)
y (open)
x | y
0 | y
1 | y
x + y
y (open)
1 (closed)

## Slide 10: Canonical disjunctive normal form (CNDF)
CDNF is an algorithm of reconstructing a function from its truth table
  Take lines with 1’s in the output only
  Conjunct (ANDing) all variables in each line with a correct sign
  Make disjunction (ORing) on the expressions
x | y | z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
!x !y !z
!x y z
x !y !z
x y !z
F = (!x !y !z) + (!x y z) + (x !y !z) + (x y !z)
F
1
0
0
1
1
0
1
0
By construction, this expression gives 1 only for these values of the arguments and 0 for all the others
Due to ORing 0’s in other terms do not prevent 1 from propagating to the output
→ Hint: use CNFG if there are less 1’s than 0’s

## Slide 11: Canonical conjunctive normal form (CCDF)
CCNF is an algorithm of reconstructing a function from its truth table
  Take lines with 0’s in the output only
  Make disjunction (ORing) of all variables in line with correct sign
  Make conjunction (ANDing) on the expressions
x | y | z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
x + y + !z
x + !y + z
!x + y + !z
!x + !y + !z
F = (x + y + !z)(x + !y + z)(!x + y + !z) (!x + !y + !z)
F
1
0
0
1
1
0
1
0
By construction, this expression gives 0 only for these values of the arguments and 1 for all the others
Due to ANDing 1’s in other terms do not prevent 0 from propagating to the output
→ Hint: use CCFG if there are less 0’s than 1’s

## Slide 12: Karnaugh Map
Karnaugh maps help to facilitate a simplification process of Boolean functions
Maurice Karnaugh
(1924)
American physicist and mathematician
 | A | B | C | D
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
 | 0 | 0 | 1 | 1
 | 0 | 0 | 1 | 1
 | 0 | 0 | 0 | 1
 | 0 | 1 | 1 | 1
A B
C D
F =
Fig.: Karnaugh map
00
01
11
10
00
01
11
10
1
1
0
0
0
0
0
1
0
0
0
1
1
1
1
1
+ !B !C
+ A !B
B C !D
There are no borders. Rectangles can cross them to form larger rectangles.
Row and columns are ordered in Gray Code: adjacent values differ only by a single bit.
F
1
1
0
0
0
0
1
0
1
1
1
1
0
0
1
0
Algorithm:
  Cover all ones by minimal number of rectangles
  Length of each side of the rectangles must be power of two (1, 2, 4 and so on)
  Each rectangle must be as large as possible
  Each rectangle is a term in CDNF, but without variables that change their values inside the rectangle

## Slide 13: Combinational Circuits
If the output of a function is completely defined by the current input then the function is called combinational:
Q = F(x, y, z, …)
Combinational circuit (scheme) is an implementation of a combinational function
Such circuit does not depend on its previous output
  Has no state
  Cannot remember data

## Slide 14: Comparator
Two binary numbers are equal if their bits are equal
Comparator returns true if numbers are equal
x0 | x1 | y0 | y1
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 1 | 1
… | … | … | …
Q = !x0 !x1 !y0 !y1 + x0 !x1 y0 !y1 + !x0 x1 !y0 y1 +
x0 x1 y0 y1
= !x0 !y0 (!x1 !y1 + x1 y1) + x0 y0 (x1 y1 + !x1 !y1)
= (!x0 !y0 + x0 y0) (!x1 !y1 + x1 y1)
= !(x0 !y0 + !x0 y0) * !(x1 !y1 + !x1 y1)
= !(x0  y0) * !(x1  y1)
x | y
0 | 0
0 | 1
1 | 0
1 | 1
Fig.: XOR truth table
Fig.: 2-bit digits comparator truth table
Q
1
1
1
1
0
x  y = !x y + x !y
= !(x0  y0) * !(x1  y1)
x0
y0
x1
y1
Q
x  y
0
1
1
0

## Slide 15: Multiplexor
Multiplexor (mux) transfers one of the data input to the output according to the control input
x
y
Q
c
x | y | c
1 | 0 | 0
0 | 1 | 1
1 | 1 | 0
1 | 1 | 1
… | … | …
M = x !y !c + !x y c + x y !c + x y c
= x !c (!y + y) + y c (!x + x)
= x !c + y c
Fig.: mux truth table
M
1
1
1
1
0
x
c
y
M
Fig.: mux notation
Fig.: mux circuit

## Slide 16: 4-input Multiplexor
A0
A1
d0
d1
d2
d3
D0
D1
D2
D3
M
A0 | A1
0 | 0
0 | 1
1 | 0
1 | 1
A0 | A1
0 | 0
1 | 0
0 | 1
1 | 1
d0 | d1 | d2 | d3
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
Fig.: 4-in-1 mux truth table
Fig.: decoder truth table
M
D0
D1
D2
D3

## Slide 17: Half Bit Adder
carry
sum
Half
x | y
0 | 0
0 | 1
1 | 0
1 | 1
0
1
1
0
0
0
0
1
carry
x
y
sum
HBA
y
x
sum
carry
Fig.: bit adder truth table
Fig.: bit adder circuit
Fig.: bit adder notation
However, it is a half bit adder (HBA) as an input carry is not accounted
  The multi-digit adder cannot be build based on it
H

## Slide 18: Full Adder
FBA
y
x
sum
carry
c
cn
FBA
yn
xn
cn-1
sn
FBA
yn+1
xn+1
cn+1
sn+1
HBA
yn
xn
cn-1
HBA
sn
Cn

## Slide 19: Questions?