## Slide 1: Finite State Machines Part 2
Igor Smirnov

## Slide 2: Recap: Finite State Machines
FSM: A system that visits a finite number of logically distinct states
  Abstract away combinational and sequential logic into functions
  These functions take in a stream of bits, do something with them, and output something deterministic
A convenient way to conceptualize computation over time
Function can be represented with a state transition diagram
With combinational logic and registers, any FSM can be implemented in hardware

## Slide 3: Moore and Mealy FSMs
There are two different ways to implement FSM with respect to the output: Moore and Mealy
Different implementation of the output logic:
Mem
Output
Next State
Input
Output
Mem
Output
Next State
Input
Output
Moore: output depends on the current state only
Mealy: output depends on the current state and on the input
Notes: Comparison of Mealy machines and Moore machines
1. Mealy machines tend to have fewer states:
  - Different outputs on arcs (n2) rather than states (n).
2. Moore machines are safer to use:
  - Outputs change at clock edge (always one cycle later).
  - In Mealy machines, input change can cause output change as soon as logic is done—a big problem when two machines are interconnected – asynchronous feedback may occur if one isn't careful.
3. Mealy machines react faster to inputs:
  - React in same cycle—don't need to wait for clock.
  - In Moore machines, more logic may be necessary to decode state into outputs—more gate delays after clock edge.

## Slide 4: Lecture 5: Sequence Analyzer (Moore)
  Output 1 if the previous three inputs are 011 or 110
Below is the minimal form received by the row matching approach
Input Sequence | Present State | Next State |  | Output
 |  | In=0 | In=1 | 
0 | S0 | Sno | S01 | 0
1 | S1 | Sno | S11 | 0
00/10 | Sno | Sstart | Sstart | 0
01 | S01 | Sstart | Syes | 0
11 | S11 | Syes | Sstart | 0
Not 011/110 or Reset | Sstart | S0 | S1 | 0
011/110 | Syes | S0 | S1 | 1
start
[0]
1
[0]
no
[0]
11
[0]
1
0
1
0
1
0
1
0
[0]
01
[0]
0
1
1
0
yes
[1]
0
1
0
Sequence Analyzer FSM
Sequence
1
Match
1

## Slide 5: Sequence Analyzer: Moore vs. Mealy
start
[0]
1
[0]
no
[0]
11
[0]
1
0
1
0
1
0
1
0
[0]
01
[0]
0
1
1
0
yes
[1]
0
1
0
start
1
no
11
1/0
0/0
1/0
0/0
0/1
1/0
0
01
0/0
1/0
0/0
1/0
0/0
1/1
Fig.: Moore state diagram
Fig.: Mealy state diagram
What is the difference between start and yes states? → only output
state
output
input
state
output
input
Notes: Moore Machine –
1. Output depends only upon present state.
2. If input changes, output does not change.
3. More number of states are required.
4. There is more hardware requirement.
5. They react slower to inputs(One clock cycle later)
6. Synchronous output and state generation.
7. Output is placed on states.
8. Easy to design.
Mealy Machine –
1. Output depends on present state as well as present input.
2. If input changes, output also changes.
3. Less number of states are required.
4. There is less hardware requirement.
5. They react faster to inputs.
6. Asynchronous output generation.
7. Output is placed on transitions.
8. It is difficult to design.

## Slide 6: FSM Design
FSM design procedure
  Step 1: State transition diagram
  Step 2: State transition table
  Step 3: State minimization
  Step 4: State encoding
  Step 5: Next-state functions
  Step 6: Schematic
Row matching
Implication table

## Slide 7: Row Matching Limitations
S1
[0]
S2
[0]
1
S0
[0]
1
0
1
S3
[1]
S4
[1]
0
0
1
1
0
0
S5
[0]
1
0
The following FSM cannot be further minimized via row matching
Current state | Input | Next state | Output
S0 | 0 | S1 | 0
 | 1 | S2 | 
S1 | 0 | S3 | 0
 | 1 | S1 | 
S2 | 0 | S3 | 0
 | 1 | S2 | 
S3 | 0 | S5 | 1
 | 1 | S1 | 
S4 | 0 | S5 | 1
 | 1 | S2 | 
S5 | 0 | S0 | 0
 | 1 | S4 | 
Is this the most reduced FSM?
→ In fact, no
Row matching does not guarantee the most reduced FSM 
Notes: Equivalent States: for all input combinations, states transition to the same or equivalent states

## Slide 8: Implication Table Method: step 1
S1
[0]
S2
[0]
1
S0
[0]
1
0
1
S3
[1]
S4
[1]
0
0
1
1
0
0
S5
[0]
1
0
Current state | Input | Next state | Output
S0 | 0 | S1 | 0
 | 1 | S2 | 
S1 | 0 | S3 | 0
 | 1 | S1 | 
S2 | 0 | S3 | 0
 | 1 | S2 | 
S3 | 0 | S5 | 1
 | 1 | S1 | 
S4 | 0 | S5 | 1
 | 1 | S2 | 
S5 | 0 | S0 | 0
 | 1 | S4 | 
S0
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4
S5

## Slide 9: Implication Table Method: step 2
S1
[0]
S2
[0]
1
S0
[0]
1
0
1
S3
[1]
S4
[1]
0
0
1
1
0
0
S5
[0]
1
0
Current state | Input | Next state | Output
S0 | 0 | S1 | 0
 | 1 | S2 | 
S1 | 0 | S3 | 0
 | 1 | S1 | 
S2 | 0 | S3 | 0
 | 1 | S2 | 
S3 | 0 | S5 | 1
 | 1 | S1 | 
S4 | 0 | S5 | 1
 | 1 | S2 | 
S5 | 0 | S0 | 0
 | 1 | S4 | 
S0
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4
S5
0
0
1
1
0
0
1
1
0
1
1
0
1
0
0
0
0
0
1
1
0
0
0
1
0
0
0
0
0
0
Notes: Implication Chart Filling in the Implication Chart Entry Xij — Row is Si, Column is Sj Si is equivalent to Sj if outputs are the same and next states are equivalent
Xij contains the next states of Si, Sj which must be equivalent if Si and Sj are equivalent If Si, Sj have different output behavior, then Xij is crossed out

## Slide 10: Implication Table Method: step 3
S1
[0]
S2
[0]
1
S0
[0]
1
0
1
S3
[1]
S4
[1]
0
0
1
1
0
0
S5
[0]
1
0
Current state | Input | Next state | Output
S0 | 0 | S1 | 0
 | 1 | S2 | 
S1 | 0 | S3 | 0
 | 1 | S1 | 
S2 | 0 | S3 | 0
 | 1 | S2 | 
S3 | 0 | S5 | 1
 | 1 | S1 | 
S4 | 0 | S5 | 1
 | 1 | S2 | 
S5 | 0 | S0 | 0
 | 1 | S4 | 
S0
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4
S5
S3
S1
S3
S2
S0
S4
S3
S2
S5
S2
S0
S4
S0
S4
S1
S2
S1
S2
S1
S2
S3
S1
S3
S1
S3
S2
S5
S1
S3
S3
S0
S1
S1
S0
S0
S3
S1
S3

## Slide 11: Implication Table Method: step 4
S0
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4
S5
S3
S1
S3
S2
S0
S4
S3
S2
S5
S2
S0
S4
S0
S4
S1
S2
S1
S2
S1
S2
S3
S1
S3
S1
S3
S2
S5
S1
S3
S3
S0
S1
S1
S0
S0
S3
S1
S3
S1’
[0]
S0
[0]
0, 1
1
S3’
[1]
0
S5
[0]
0
1
1
0
S1
[0]
S2
[0]
1
S0
[0]
1
0
1
S3
[1]
S4
[1]
0
0
1
1
0
0
S5
[0]
1
0

## Slide 12: FSM Design
FSM design procedure
  Step 1: State transition diagram
  Step 2: State transition table
  Step 3: State minimization
  Step 4: State encoding
  Step 5: Next-state functions
  Step 6: Schematic

## Slide 13: State Encoding Problem
Task: choose bit vectors to assign to each “symbolic” state
  With n state bits for m states there are 2n! / (2n – m)! restrictions for n is [log n <= m <= 2n]
    2n codes possible for 1st state, 2n–1 for 2nd, 2n–2 for 3rd, …
Huge number even for small values of n and m
  Intractable for state machines of any size
  Heuristics are necessary for practical solutions
Optimize some metric for the combinational logic
  Size (amount of logic and number of FFs)
  Speed (depth of logic)
Notes: When FSM implemented with gate logic, number of gates will depend on mapping between symbolic state names and binary encodings 4 states = 4 choices for first state, 3 for second, 2 for third, 1 for last = 24 different encodings (4!)

## Slide 14: State-encoding strategies
No guarantee of optimality
  An intractable problem
Most common strategies
  Binary (sequential) – number states as in the state table
  Random – computer tries random encodings
  Heuristic – rules of thumb that seem to work well
    e.g. Gray-code – try to give adjacent states (states with an arc between them) codes that differ in only one bit position
  One-hot – use as many state bits as there are states
  Output – use outputs to help encode states
  Hybrid – mix of a few different ones (e.g. One-hot + heuristic)

## Slide 15: One-hot encoding
One-hot: Encode n states using n flip-flops
  Assign a single “1” for each state
    Example: 0001, 0010, 0100, 1000
  Propagate a single “1” from one flip-flop to the next
    All other flip-flop outputs are “0”
The inverse: One-cold encoding
  Assign a single “0” for each state
    Example: 1110, 1101, 1011, 0111
  Propagate a single “0” from one flip-flop to the next
    All other flip-flop outputs are “1”
“almost one-hot” encoding (modified one-hot encoding)
  Use no-hot (000…0) for the initial (reset state)
  Assumes you never revisit the reset state till reset again.

## Slide 16: One-hot encoding (con’t)
Often the best/convenient approach for FPGAs
  FPGAs have many flip-flops
Draw FSM directly from the state diagram
  + One product term per incoming arc
  - Complex state diagram  complex design
  - Many states  many flip flops
One-hot encoding typically enables higher frequency vs other encoding strategies
See details: https://www.sciencedirect.com/topics/computer-science/one-hot-encoding

## Slide 17: Orgs
Next lecture: Nov 3
Topic: Arithmetic Circuits