## Slide 1: Digital Integrated Circuits Design Lecture 1: Introduction
Igor Smirnov

## Slide 2: Intro
Who am I?
  Hardware Architect
  10 years in hardware industry
  5 years of teaching experience
Why are we here?
  To study key concepts in the circuit design (CD) – major part of Computer Engineering
  To better understand modern design tradeoffs and limitation
  Useful even for “SW persons”: it is always good to see “the whole picture”
  BTW, it is about how Intel makes money

## Slide 3
ONE DOES NOT SIMPLY
STUDY COMPUTER ENGINEERING

## Slide 4: Layers of Abstractions in Computer Engineering
Hardware (HW)
Software (SW)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Register-Transfer Level (RTL)
Gates
Devices (Transistors)
Circuits
Physics
Interface between HW and SW
Computer Science
(CS)
Electrical Engineering
(EE)
Pavel Kryukov
Andrey Dobrov
Your courses this year:
This course

## Slide 5: This course focus
Register-Transfer Level (RTL)
Gates
Devices (Transistors)
Circuits
Physics
Microarchitecture

## Slide 6: Reminder: Perf, Power, Cost

## Slide 7: Basic Design Tradeoffs
CE Triangle
All three are very important
It is extremely hard to create a feature that improves all of them
Different products (mobile, server, etc.) require different balances
Performance
(speed)
Cost
(complexity, area)
Energy
and
Power

## Slide 8: Performance
What does performance depend on?
Performance Golden Rule
Clocks Per Instruction
Instructions Per Clock

## Slide 9: Increasing Performance
How can we increase it?
SW: algorithms, optimizations, ISA, etc.
CD: faster circuits, smaller transistors, etc.
uArch: pipelining, caching, prediction, etc.
But, CD enables these approaches
(e.g., more transistors)

## Slide 10: Energy Consumption
Why is power important?
  Less power -> smaller battery -> smaller/cheaper devices
  Less power -> less money for electricity
Power Wall is reached
  The maximum power dissipation that cooling systems can handle is reached
  We cannot spend more power even
  if we want
Nuclear reactor? No, power supply for a large data center

## Slide 11: Energy
Why is energy per task important?
  Battery life of a device
  Less energy -> longer battery life or smaller battery
  Smaller battery -> smaller devices (e.g., wearables)
  Electricity bills
  Less energy -> less money for electricity
  Huge expense item for large data centers
A nuclear reactor?
No, power supply for a large data center

## Slide 12: Power
Why is power important?
  Power Wall has been reached
  Reasonable cooling systems cannot handle more power
  New reality: we cannot spend more power even if we want
Too expensive and unreliable
Power Wall

## Slide 13: Dynamic Power
Two components: dynamic + static
Dynamic power is caused by changing an input signal
  It looks like we repeatedly recharge capacitors
How to decrease it?
Better uArch and CD:
decrease number of transistors and wires,
decrease number of signal changes
Decrease frequency…
but it decreases performance
Decrease voltage…
but it decreases transistor switching speed -> makes us decrease frequency -> decrease performance

## Slide 14: Static Power
Two components: dynamic + static
Static power is caused by leakage currents in transistors
  The smaller transistor the larger leakage
  It is roughly proportional to chip area
How to decrease static power?
  Switch off unused transistors (power gating)
  New types of transistors (e.g., Intel’s 3d transistor)
  New types of materials

## Slide 15: Cost
Fixed Cost (RnD)
  Independent of volume (i.e., number of units made/sold)
  Examples: design time and effort, mask generation, etc.
Variable Cost (manufacturing/production)
  proportional to volume
  Examples: silicon processing, packaging, test
  Most of these related to chip area
The larger chip size the large production cost
  Less chips on one wafer
  Larger probability of error
Yield = 1/4
Yield = 19/24

## Slide 16: Questions?
CS Triangle
Performance
(speed)
Cost
(complexity, area)
Energy
and
Power

## Slide 17: Orgs
9-10 lectures in semester
2 tests
  1 attempt / test
  Tests take one lecture slot
Final score is an average of 2 tests
Course materials: https://github.com/igorsmir-ilab/public
Contact mail: igor.smirnov@phystech.edu